## Slide 1: Wide BVH traversal with a short stack
Karthik Vaidyanathan, Sven Woop, Carsten Benthin

## Slide 2: Motivation
Ray tracing hardware acceleration easily constrained by memory bandwidth
Compressed wide BVHs can reduce node bandwidth [Wald et al. 14, Ylitie et al. 17]
Lossless meshlet compression can reduce geometry bandwidth
Full stack can add additional bandwidth when stored to memory when procedural geometry is intersected
 Need stack algorithm for wide BVHs with compact state

## Slide 3: Previous Work
Stackless traversal with skip pointers [Smits 98]
  Enforces a fixed traversal order
Stackless traversal with backtracking to parent [Hapala et al. 11, Afra et al. 14]
  Allows front to back order
  Needs to re-intersect parent node
Binary BVH traversal with a restart trail [Laine 10]
  Maintain a restart trail and short stack of topmost entries
  Restart from root on an short stack underflow
skip
parent

## Slide 4: BVH Traversal with a Restart Trail
A restart trail with short stack is well suited for fixed function ray tracing
  Short stack entries and the restart trail small
  Low overhead (10%) as short stack avoids most redundant traversal steps
  Our Wide-BVHs restart trail algorithm builds on binary BVH traversal of [Laine 10]

## Slide 5: Binary BVH Traversal with a Restart Trail
Assuming fixed front to back ordering of child nodes along the ray
Restart trail is bit vector (and depth) that encodes processed part of BVH
RestartTrail[level] == 0 indicates that the first child is being traversed
RestartTrail[level] == 1 indicates that the last child at the given level is being traversed
 Pop operations can easily skip over finished levels

## Slide 6: Binary Restart Trail
0
0
0
LEVEL = 3
Restart Trail
Find closest level < 1
Increment
1
LEVEL = 1
1
1
0
0
clear

## Slide 7: N-Wide BVH Traversal with a Restart Trail
Assuming fixed front to back ordering of child nodes along the ray
Restart trail is an integer vector (and depth) that encodes processed part of BVH
RestartTrail[level] indicates the n’th child currently traversed
RestartTrail[level] set to N-1 indicates the last child subtree being traversed
 Pop operations can easily skip over finished levels

## Slide 8: Detecting the Last Child
During down traversal the last child at a given level is detected when RestartTrail[level] == (number of intersections – 1)
But we do not know if an entry popped from the short stack is the last child
Therefore we use one additional bit per short stack entry to mark the last child when it is pushed onto the stack.
Not required for binary BVH as popped nodes are always the last node.

## Slide 9: Example 4-Wide BVH Traversal
0
0
0
0
0
LEVEL = 0
Restart Trail
Short Stack
(3 Entries )

## Slide 10: Example 4-Wide BVH Traversal
A
0
0
0
0
0
LEVEL = 0
Restart Trail
Short Stack
(3 Entries )
C
B
C
Last Child
B
C
B

## Slide 11: Example 4-Wide BVH Traversal
A
0
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
LEVEL = 1
C
B

## Slide 12: Example 4-Wide BVH Traversal
A
D
0
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
LEVEL = 1
E
F
C
B
E
F
Last Child
C dropped

## Slide 13: Example 4-Wide BVH Traversal
A
D
0
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
B
C
B
E
F
E
F
B
LEVEL = 2
E
E Popped
1
Increment
Find closest level < 3
D

## Slide 14: Example 4-Wide BVH Traversal
1
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
B
C
B
E
F
B
F
LEVEL = 2
F
3
Set to 3
last child
F Popped
Find closest level < 3
E

## Slide 15: Example 4-Wide BVH Traversal
A
D
3
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
B
C
B
E
F
B
LEVEL = 3
F
G
3
Set to 3
last child

## Slide 16: Example 4-Wide BVH Traversal
A
D
3
3
0
0
0
Restart Trail
Short Stack
(3 Entries )
B
C
B
E
F
Find closest level < 3
G
LEVEL = 3
1
Increment
0
0
clear

## Slide 17: Example 4-Wide BVH Traversal
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
B
C
B
E
F
G
LEVEL = 1
B Popped
B
1
Find closest level < 3
2
Increment

## Slide 18: Example 4-Wide BVH Traversal
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
G
LEVEL = 0
B
2
Stack empty: restart

## Slide 19: Example 4-Wide BVH Traversal
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
G
LEVEL = 0
B
2

## Slide 20: Example 4-Wide BVH Traversal
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
G
LEVEL = 1
B
3
Set to 3
last child

## Slide 21: Example 4-Wide BVH Traversal
A
D
0
0
0
0
Restart Trail
Short Stack
(3 Entries )
C
B
E
F
G
LEVEL = 1
B
3
Find closest level < 3

## Slide 22: Results for 6-wide BVH
Chart: traversal steps
| Bathroom | Crown | SanMiguel | Villa | Classroom | BMW
SHORT_1 | 15.444 | 32.129 | 52.898 | 20.006 | 18.332 | 9.168
SHORT_2 | 13.163 | 24.465 | 39.998 | 17.27 | 15.718 | 7.675
SHORT_3 | 12.396 | 21.182 | 34.571 | 16.187 | 14.699 | 7.092
SHORT_4 | 12.087 | 19.606 | 31.837 | 15.672 | 14.224 | 6.795
SHORT_5 | 11.938 | 18.601 | 30.313 | 15.422 | 13.939 | 6.675
FULLSTACK | 11.773 | 16.938 | 27.757 | 15.149 | 13.771 | 6.644

## Slide 23: Stack culling
Storing near distance on the short stack would allow culling of popped nodes when a closer hit was found
 memory overhead
Alternatively one can process closest child and push the parent node onto the short stack for later re-intersection
 small culling overhead but often pays off

## Slide 24: Conclusions
Presented short stack with restart trail for wide BVHs
Allows very compact stack storage at minimal overhead
Suitable for fixed function ray tracing implementations